Flux phi	(~current)

Magnetic Lines of Force
Mx (maxwell) one line of force	cgs
Wb (weber) 108 lines of force	mks
uWb (microweber) 100 lines of force

Flux Density B	(~current)
Lines of Force per Area
Mx/cm2 = G (gauss)	cgs
Wb/m2 = T (tesla)	mks

Reluctance R
Resistance to flow of Flux or Flux Density
Like Resistance
H/R = B
Field Strength/Reluctance = Flux Density
mmf/R =

Field/Reluctance = Flux

Permeability u
Acceptance to flow of Flux or Flux Density
Like Conductance
H *u = B
Field Strength * Permeability =Flux Density
mmf *u =

Field * Permeability = Flux

Relative Permeability ur for SI units Tesla, At/m
ur * 1.26*10-6 = u
H * ur * 1.26*10-6 = B

Field mmf (MagnetoMotive Force)	(~voltage)
A*t (amps times turns)	mks
Gb (gilbert)	cgs
1At = 1.26Gb = (4pi/10)Gb

Field Strength H	(~voltage)
A*t/meter	mks
Gb/cm = Oe (oersted)	cgs